NA-DVR32224 32 CHANNEL PC-BASED DVR 240 fps display & Recording 16 audio inputs Remote viewing over internet Composite 2nd monitor output

Display FPS 240 Record FPS 240 (at 1CIF) Video Channels 32 BNC-M Audio Channels 16 RCA-F Record Resolution 1CIF: 352x240, 2CIF: 704x240, 4CIF: 704x480 Compression Proprietary Enhanced MJPEG (2~7kb/ frame at 1CIF) Video Input Voltage 1 Vpp CVBS Video Input Impedance 75 Ohms (hi-impedance x 16 switchable) Video Recording Format analog line-in, 11 KHz sampling rate Monitor Output 1 x VGA DB9, 1280x1024, 32 Bit, 70 Hz Spot Monitor Output 1 x BNC-M, 32 split only, no switching USB Output 2 x front, 2 x rear RS232 1 x DB9-M (RS232/485 converter required for PTZ) Network 1 x 10/100 NIC onboard Audio Out 1 x Speaker Out Media Writer 1 x CDRW Drive * Above specification and design subject to change without notification